## Slide 1
Energy Management of Parallel Mild Hybrid Electric Vehicle
Jeinil Patel (407374)
Nihal Oza (407633)
Brijesh Varsani (407342)
Guided by
Jun.-Prof. Dr – Ing. Daniel Görges
Seminar Electromobility SS 2018
Commercial Vehicle Technology

## Slide 2: Contents
Introduction
    Definitions
    Advantages and Disadvantages
Architectures of Hybrid Electric Vehicles
Operation Modes
Driving cycles
Energy management system
Tool box and controller
Vehicle operation modes
Simulation results
Conclusion

## Slide 3: Introduction
Definition: Hybrid Vehicle(HV) means a vehicle with at least two different energy converters and two different energy storage systems (on vehicle) for the purpose propulsion
Hybrid Electric Vehicle
Hybrid Vehicle
Definition: Hybrid electric vehicle (HEV) means a vehicle that, for the purpose of mechanical
propulsion, draws energy from both of the following on-vehicle sources of stored energy/power:
  a consumable fuel
  an electrical energy/power storage device (e.g. battery, capacitor, flywheel/generator, etc.).

## Slide 4
Advantages and Disadvantages of HEVs
    Help reduce the consumption of fossil fuel and work towards ecofriendly driving.
    It minimize the emission of greenhouse gases.
    With electric source supplementing the ICE, fuel consumption is reduced, making it fuel efficient.
    With strict legislative regulation , incentives with tax benefits are provided to encourage electric vehicles.
Advantages
Disadvantages
    The discharge of power is fast which makes it not reliable for long distance travel.
    The quantity of charge that can be stored is limited .
    The no. of times battery can be charged and discharged is limited causing limited battery life.
    Requires many safety instrument to avoid any accidents due to the high voltage system.
    Due to high safety and maintenance factor it is expensive compared to conventional vehicle.
Introduction

## Slide 5
Series Hybrid Vehicle
  In series hybrid vehicle, the engine is not directly connected to the transmission
  Power from engine is transmitted through the motor
Parallel Hybrid Vehicle
  Parallel hybrid vehicle consist of ICE and Electric power supply connected in parallel to the mechanical transmission system
  It is found to be very compact as there are only two propulsion devices to power the wheels
Architecture of HEV

## Slide 6
Combined Hybrid Vehicle
  It has features of both Series and Parallel HEVs
  Medium energy conversion losses
  Medium production cost and weight
  High complexity
Parallel mild Hybrid Vehicle
  The power to the wheel is generated by combining a conventional ICE propulsion system with an electric drive system
  As motor is not connected to the engine directly, it is efficient during start/stop mode of the vehicle
  The electric motor can work both as generator during regeneration and as motor during electric driving
Architecture of HEV

## Slide 7
Engine Start/Stop
  Engine consumes more fuel during idling
  Stopping the engine instead of idling can substantially decrease fuel consumption
Regeneration
  Kinetic energy is dissipated to heat in friction braking and engine braking
  Kinetic energy can be stored in the battery by using the motor as generator in regenerative braking
Driving mode

## Slide 8
Engine load Point Shifting (0 ≤ 𝑢 < 1 : Motor mode; 𝑢 < 0 : Generator mode)
  Engine efficiency strongly depends on the load (low efficiency at low loads due to throttling losses etc.)
  Pollutant emissions also strongly depend on the load
  Engine efficiency and pollutant emissions can be improved by shifting the load with the motor
  Load can be increased by operating the motor in generator mode and charging the battery
  Load can be decreased by operating the motor in motor mode and discharging the battery
(i)Motor Mode
(ii)Generator Mode
Driving mode

## Slide 9: Driving mode
Electric Driving (𝑢 = 1)
  Engine efficiency is very low at very low loads (e.g. in cities at low speeds)
  Electric driving at very low loads and recharging the battery at low and intermediate loads
  Electric driving can then be considered as a variant of engine load point shifting
Conventional Driving (𝑢 = 0 )
In conventional driving, only combustion engine provides torque for the wheels

## Slide 10
      EU New European Driving Cycle (NEDC)
        New European Driving Cycle (NEDC) is the European standard for operation and control of emission in passenger vehicles
        Set to control the emission of greenhouse gases and fuel consumption. Low to moderate torque expectation
        Consists of four repeated urban driving cycles (UDC) and one Extra-Urban driving cycle (EUDC)
      EPA Federal Test Procedure (FTP-75)
        It is the vehicle standard implemented in America and its neighboring countries
        US Environmental Protection Agency (EPA) is the organization that defines the standard for the vehicle
        The tests are based on different road condition with city roads and highways
        The procedure contains the “cold star’’ at the beginning, then “stabilized phase” and “hot start" cycle at the end
Driving cycles

## Slide 11
Different strategies can be implemented
Energy management strategy

## Slide 12
Rule based strategy requires less computational time when compared to Dynamic Programming(DP)
It is based on concept of load leveling and state of charge
The load level strategy is to shift the ICE operating point close to optimal point of efficiency or emission at particular speed
In this strategy the ICE is used as the primary source of power and the BT is used as secondary source
Both the sources are used as per different power, torque and efficiency
For low torque requirements, only the motor is used provided that battery charge is sufficient
Engine shuts off when the power demand falls below a limit at the operating speed to prevent inefficient operation
If the demanded power is greater than the maximum engine power at its operating speed, the motor is used to produce excess power
  Rule Based Control Strategy
Proposed control strategy

## Slide 13
The Quasi Static Simulation (QSS) toolbox gives the flexibility to design the powertrain systems quickly and calculate the fuel consumption of different systems under different strategies
QSS Toolbox

## Slide 14
Controller structure
The controller block consist of controller that is designed for start-stop of engine and other mode (Electric driving, regeneration, etc.)
    Angular velocity, gearbox torque, angular acceleration and battery charge are used as input
Controller

## Slide 15
    Regeneration
  Requirements
    Kinetic energy can be stored in battery by regenerative braking
    The constraint of the engine T_MGB < 0 must be regarded
  Results
    The motor works as generator and stores maximum possible energy
    Start/Stop mode
  Requirements
      Constraint of the engine, T_MGB < 0, 0 < T_MGB < 29, must be regarded
      Constraint of the battery, SoC > 0.35 , must be regarded
  Results
      If these constraints result as true then 𝑠𝑡𝑎𝑡𝑒_CE= 0, i.e. combustion engine will be stopped
      This in turn will enforce the fuel cutoff in engine
      If the above constraints are false then 𝑠𝑡𝑎𝑡𝑒_CE= 1, i.e. combustion engine will be started
Vehicle operation mode

## Slide 16
  Motor mode
    Requirements
      The constraint of the engine T_MGB > T_MGB_th must be regarded
      The constraint of the battery SoC > 0.8, must be regarded
    Results
      The load point can be decreased by operating the motor in motor mode
Load point shifting
      The efficiency improvement must be larger than conversion losses suggesting an optimization
  Generator mode
    Requirements
      The constraint of the engine T_MGB > T, T_MGB < T_MGB_th must be regarded
    Results
      The load point can be increased by operating the motor in generator mode
Vehicle operation mode

## Slide 17
    Electric drive
  Requirements
    The efficiency improvement must be larger than charging losses suggesting an optimization
    The constraint of the engine T_MGB > 0, T_MGB < T must be regarded
    The constraint of the battery SoC > 0.35 must be regarded
  Results
    The electric driving at low load points can improve the efficiency
    Engine drive
  Requirements
      The vehicle will be in this mode if none of the above constraints are satisfied
      The constraint, Torque split ratio 𝑢 = 0, is regarded
  Results
    The engine driving can then be considered as a variant of load point shifting
Vehicle operation mode

## Slide 18
Results for NEDC cycle
Results for NEDC Cycle
State of charge vs time
Torque split ratio vs time
    From the simulation graph of State of charge vs. Time we can say :
    ICE and electric motor optimize the power balance
    Charge is sustained at later part of driving cycle.
    System charges and discharges at various mode of operation.
    Smooth operation at start and stop mode.
Charge sustained

## Slide 19
Results for NEDC Cycle
Gear box torque vs time
Fuel efficiency vs time
    From the graph of Fuel efficiency and Gearbox torque Vs. Time :
    We can observe reduction in fuel consumption in Parallel HEVs at later stage of driving.
    The torque graph describes the braking and acceleration during the cycle .
    At the end, it is found that system is in regenerative mode .
Results for NEDC cycle

## Slide 20
Torque split ratio vs time
Results for FTP-75 Cycle
State of charge vs time
    From the following simulation graph of State of charge vs. Time we can say :
    ICE and electric motor optimize the power balance
    Charge is marginally sustained at end of the cycle.
    Start-stop is frequent compared to NEDC cycle.
Results for FTP-75 cycle

## Slide 21
Fuel efficiency vs time
Results for FTP-75 Cycle
Gear box torque vs time
    From the graph of Equivalent Fuel Consumption and Torque Vs. Time :
    We can observe reduction in fuel consumption in Parallel HEVs at later stage of driving.
    The torque graph describes the braking and acceleration during driving
    At the end, it is found that system is in regenerative mode .
Results for FTP-75 cycle

## Slide 22
Parameters | NEDC Cycle | FTP-75 Cycle
 | 18010 | 18010
(liters/100 km) Conventional Vehicle | 4.897 | 4.675
(liters/100 km) Hybrid Vehicle | 3.56 | 3.283
Parameters | NEDC Cycle | FTP-75 Cycle
 | 18010 | 18010
 | 4.897 | 4.675
 | 3.56 | 3.283
27.30 %
29.77 %
25
27
29
31
% Saving
FTP-75
NEDC
Simulation Results

## Slide 23
Reference
Lino Guzzella and Antonio Sciarretta. Vehicle Propulsion Systems: Introduction to Modeling and Optimization.Springer,Heidalberg, 3rd edition,2013.
D. Görges, "Seminar Electromobility (Summer Term 2018)," Lecture Notes, Juniorprofessorship for Electromobility, Department of Electrical and Computer Engineering, University of Kaiserslautern, Kaiserslautern, Germany, 2018.
L Guzzella and A. Amstutz, The QSS Toolbox Manual, Institute for Dynamic Systems and Control, Department of Mechanical and Process Engineering, ETH Zürich , Zürich, switzerland, 2005, http://www.idsc.ethz.ch/research-guzzell-onder/downloads.html (Last call on 12 June 2018).
Michiel Koot, Bram de Jager, Maarten Steinbuch.Energy Management Strategies for Vehicular Electric Power Systems. IEEE Transactions on Vehicular Technology, Vol.54, No.3,May 2005.
Pierluigi Pisu and Giorgio Rizzoni. A Comparative Study of Supervisory Control Strategies for Hybrid Electric Vehicles. IEEE Transactions on Control Systems Technology, Vol.15, No.3, May 2007.

## Slide 24
Thank you for your attention!!